## Slide 1: Fundamentals of Microelectronics
CH1 Why Microelectronics?
CH2 Basic Physics of Semiconductors
CH3 Diode Circuits
CH4 Physics of Bipolar Transistors
CH5 Bipolar Amplifiers
CH6 Physics of MOS Transistors
CH7 CMOS Amplifiers
CH8 Operational Amplifier As A Black Box

## Slide 2
1.1 Electronics versus Microelectronics
1.2 Example of Electronic System: Cellular Telephone
1.3 Analog versus Digital
Chapter 1 Why Microelectronics?

## Slide 3: Cellular Technology
An important example of microelectronics.
Microelectronics exist in black boxes that process the received and transmitted voice signals.

## Slide 4: Frequency Up-conversion
Voice is “up-converted” by multiplying two sinusoids.
When multiplying two sinusoids in time domain, their spectra are convolved in frequency domain.

## Slide 5: Transmitter
Two frequencies are multiplied and radiated by an antenna in (a).
A power amplifier is added in (b) to boost the signal.

## Slide 6: Receiver
High frequency is translated to DC by multiplying by fC.
A low-noise amplifier is needed for signal boosting without excessive noise.

## Slide 7: Digital or Analog?
X1(t) is operating at 100Mb/s and X2(t) is operating at 1Gb/s.
A digital signal operating at very high frequency is very “analog”.

## Slide 8: Chapter 2 Basic Physics of Semiconductors
2.1 Semiconductor materials and their properties
2.2 PN-junction diodes
2.3 Reverse Breakdown

## Slide 9: Semiconductor Physics
Semiconductor devices serve as heart of microelectronics.
PN junction is the most fundamental semiconductor device.

## Slide 10: Charge Carriers in Semiconductor
To understand PN junction’s IV characteristics, it is important to understand charge carriers’ behavior in solids, how to modify carrier densities, and different mechanisms of charge flow.

## Slide 11: Periodic Table
This abridged table contains elements with three to five valence electrons, with Si being the most important.

## Slide 12: Silicon
Si has four valence electrons. Therefore, it can form covalent bonds with four of its neighbors.
When temperature goes up, electrons in the covalent bond can become free.

## Slide 13: Electron-Hole Pair Interaction
With free electrons breaking off covalent bonds, holes are generated.
Holes can be filled by absorbing other free electrons, so effectively there is a flow of charge carriers.

## Slide 14: Free Electron Density at a Given Temperature
Eg, or bandgap energy determines how much effort is needed to break off an electron from its covalent bond.
There exists an exponential relationship between the free-electron density and bandgap energy.

## Slide 15: Doping (N type)
Pure Si can be doped with other elements to change its electrical properties.
For example, if Si is doped with P (phosphorous), then it has more electrons, or becomes type N (electron).

## Slide 16: Doping (P type)
If Si is doped with B (boron), then it has more holes, or becomes type P.

## Slide 17: Summary of Charge Carriers

## Slide 18: Electron and Hole Densities
The product of electron and hole densities is ALWAYS equal to the square of intrinsic electron density regardless of doping levels.
Majority Carriers :
Minority Carriers :
Majority Carriers :
Minority Carriers :

## Slide 19: First Charge Transportation Mechanism: Drift
The process in which charge particles move because of an electric field is called drift.
Charge particles will move at a velocity that is proportional to the electric field.

## Slide 20: Current Flow: General Case
Electric current is calculated as the amount of charge in v meters that passes thru a cross-section if the charge travel with a velocity of v m/s.

## Slide 21: Current Flow: Drift
Since velocity is equal to E, drift characteristic is obtained by substituting V with E in the general current equation.
The total current density consists of both electrons and holes.

## Slide 22: Velocity Saturation
A topic treated in more advanced courses is velocity saturation.
In reality, velocity does not increase linearly with electric field. It will eventually saturate to a critical value.

## Slide 23: Second Charge Transportation Mechanism: Diffusion
Charge particles move from a region of high concentration to a region of low concentration. It is analogous to an every day example of an ink droplet in water.

## Slide 24: Current Flow: Diffusion
Diffusion current is proportional to the gradient of charge (dn/dx) along the direction of current flow.
Its total current density consists of both electrons and holes.

## Slide 25: Example: Linear vs. Nonlinear Charge Density Profile
Linear charge density profile means constant diffusion current, whereas nonlinear charge density profile means varying diffusion current.

## Slide 26: Einstein's Relation
While the underlying physics behind drift and diffusion currents are totally different, Einstein’s relation provides a mysterious link between the two.

## Slide 27: PN Junction (Diode)
When N-type and P-type dopants are introduced side-by-side in a semiconductor, a PN junction or a diode is formed.

## Slide 28: Diode’s Three Operation Regions
In order to understand the operation of a diode, it is necessary to study its three operation regions: equilibrium, reverse bias, and forward bias.

## Slide 29: Current Flow Across Junction: Diffusion
Because each side of the junction contains an excess of holes or electrons compared to the other side, there exists a large concentration gradient. Therefore, a diffusion current flows across the junction from each side.

## Slide 30: Depletion Region
As free electrons and holes diffuse across the junction, a region of fixed ions is left behind. This region is known as the “depletion region.”

## Slide 31: Current Flow Across Junction: Drift
The fixed ions in depletion region create an electric field that results in a drift current.

## Slide 32: Current Flow Across Junction: Equilibrium
At equilibrium, the drift current flowing in one direction cancels out the diffusion current flowing in the opposite direction, creating a net current of zero.
The figure shows the charge profile of the PN junction.

## Slide 33: Built-in Potential
Because of the electric field across the junction, there exists a built-in potential. Its derivation is shown above.

## Slide 34: Diode in Reverse Bias
When the N-type region of a diode is connected to a higher potential than the P-type region, the diode is under reverse bias, which results in wider depletion region and larger built-in electric field across the junction.

## Slide 35: Reverse Biased Diode’s Application: Voltage-Dependent Capacitor
The PN junction can be viewed as a capacitor. By varying VR, the depletion width changes, changing its capacitance value; therefore, the PN junction is actually a voltage-dependent capacitor.

## Slide 36: Voltage-Dependent Capacitance
The equations that describe the voltage-dependent capacitance are shown above.

## Slide 37: Voltage-Controlled Oscillator
A very important application of a reverse-biased PN junction is VCO, in which an LC tank is used in an oscillator. By changing VR, we can change C, which also changes the oscillation frequency.

## Slide 38: Diode in Forward Bias
When the N-type region of a diode is at a lower potential than the P-type region, the diode is in forward bias.
The depletion width is shortened and the built-in electric field decreased.

## Slide 39: Minority Carrier Profile in Forward Bias
Under forward bias, minority carriers in each region increase due to the lowering of built-in field/potential. Therefore, diffusion currents increase to supply these minority carriers.

## Slide 40: Diffusion Current in Forward Bias
Diffusion current will increase in order to supply the increase in minority carriers. The mathematics are shown above.

## Slide 41: Minority Charge Gradient
Minority charge profile should not be constant along the x-axis; otherwise, there is no concentration gradient and no diffusion current.
Recombination of the minority carriers with the majority carriers accounts for the dropping of minority carriers as they go deep into the P or N region.

## Slide 42: Forward Bias Condition: Summary
In forward bias, there are large diffusion currents of minority carriers through the junction. However, as we go deep into the P and N regions, recombination currents from the majority carriers dominate. These two currents add up to a constant value.

## Slide 43: IV Characteristic of PN Junction
The current and voltage relationship of a PN junction is exponential in forward bias region, and relatively constant in reverse bias region.

## Slide 44: Parallel PN Junctions
Since junction currents are proportional to the junction’s cross-section area. Two PN junctions put in parallel are effectively one PN junction with twice the cross-section area, and hence twice the current.

## Slide 45: Constant-Voltage Diode Model
Diode operates as an open circuit if VD< VD,on and a constant voltage source of VD,on if VD tends to exceed VD,on.

## Slide 46: Example: Diode Calculations
This example shows the simplicity provided by a constant-voltage model over an exponential model.
For an exponential model, iterative method is needed to solve for current, whereas constant-voltage model requires only linear equations.
for
for

## Slide 47: Reverse Breakdown
When a large reverse bias voltage is applied, breakdown occurs and an enormous current flows through the diode.

## Slide 48: Zener vs. Avalanche Breakdown
Zener breakdown is a result of the large electric field inside the depletion region that breaks electrons or holes off their covalent bonds.
Avalanche breakdown is a result of electrons or holes colliding with the fixed ions inside the depletion region.

## Slide 49: Chapter 3 Diode Circuits
3.1 Ideal Diode
3.2 PN Junction as a Diode
3.3 Applications of Diodes

## Slide 50: Diode Circuits
After we have studied in detail the physics of a diode, it is time to study its behavior as a circuit element and its many applications.

## Slide 51: Diode’s Application: Cell Phone Charger
An important application of diode is chargers.
Diode acts as the black box (after transformer) that passes only the positive half of the stepped-down sinusoid.

## Slide 52: Diode’s Action in The Black Box (Ideal Diode)
The diode behaves as a short circuit during the positive half cycle (voltage across it tends to exceed zero), and an open circuit during the negative half cycle (voltage across it is less than zero).

## Slide 53: Ideal Diode
In an ideal diode, if the voltage across it tends to exceed zero, current flows.
It is analogous to a water pipe that allows water to flow in only one direction.

## Slide 54: Diodes in Series
Diodes cannot be connected in series randomly. For the circuits above, only a) can conduct current from A to C.

## Slide 55: IV Characteristics of an Ideal Diode
If the voltage across anode and cathode is greater than zero, the resistance of an ideal diode is zero and current becomes infinite. However, if the voltage is less than zero, the resistance becomes infinite and current is zero.

## Slide 56: Anti-Parallel Ideal Diodes
If two diodes are connected in anti-parallel, it acts as a short for all voltages.

## Slide 57: Diode-Resistor Combination
The IV characteristic of this diode-resistor combination is zero for negative voltages and Ohm’s law for positive voltages.

## Slide 58: Diode Implementation of OR Gate
The circuit above shows an example of diode-implemented OR gate.
Vout can only be either VA or VB, not both.

## Slide 59: Input/Output Characteristics
When Vin is less than zero, the diode opens, so Vout = Vin.
When Vin is greater than zero, the diode shorts, so Vout = 0.

## Slide 60: Diode’s Application: Rectifier
A rectifier is a device that passes positive-half cycle of a sinusoid and blocks the negative half-cycle or vice versa.
When Vin is greater than 0, diode shorts, so Vout = Vin; however, when Vin is less than 0, diode opens, no current flows thru R1, Vout = IR1R1 = 0.

## Slide 61: Signal Strength Indicator
The averaged value of a rectifier output can be used as a signal strength indicator for the input, since Vout,avg is proportional to Vp, the input signal’s amplitude.
for
for

## Slide 62: Diode’s application: Limiter
The purpose of a limiter is to force the output to remain below certain value.
In a), the addition of a 1 V battery forces the diode to turn on after V1 has become greater than 1 V.

## Slide 63: Limiter: When Battery Varies
An interesting case occurs when VB (battery) varies.
Rectification fails if VB is greater than the input amplitude.

## Slide 64: Different Models for Diode
So far we have studied the ideal model of diode. However, there are still the exponential and constant voltage models.

## Slide 65: Input/Output Characteristics with Ideal and Constant-Voltage Models
The circuit above shows the difference between the ideal and constant-voltage model; the two models yield two different break points of slope.

## Slide 66: Input/Output Characteristics with a Constant-Voltage Model
When using a constant-voltage model, the voltage drop across the diode is no longer zero but Vd,on when it conducts.

## Slide 67: Another Constant-Voltage Model Example
In this example, since Vin is connected to the cathode, the diode conducts when Vin is very negative.
The break point where the slope changes is when the current across R1 is equal to the current across R2.

## Slide 68: Exponential Model
In this example, since the two diodes have different cross-section areas, only exponential model can be used.
The two currents are solved by summing them with Iin, and equating their voltages.

## Slide 69: Another Constant-Voltage Model Example
This example shows the importance of good initial guess and careful confirmation.

## Slide 70: Cell Phone Adapter
Vout = 3 VD,on is used to charge cell phones.
However, if Ix changes, iterative method is often needed to obtain a solution, thus motivating a simpler technique.
Ix

## Slide 71: Small-Signal Analysis
Small-signal analysis is performed around a bias point by perturbing the voltage by a small amount and observing the resulting linear current perturbation.

## Slide 72: Small-Signal Analysis in Detail
If two points on the IV curve of a diode are close enough, the trajectory connecting the first to the second point is like a line, with the slope being the proportionality factor between change in voltage and change in current.

## Slide 73: Small-Signal Incremental Resistance
Since there’s a linear relationship between the small signal current and voltage of a diode, the diode can be viewed as a linear resistor when only small changes are of interest.

## Slide 74: Small Sinusoidal Analysis
If a sinusoidal voltage with small amplitude is applied, the resulting current is also a small sinusoid around a DC value.

## Slide 75: Cause and Effect
In (a), voltage is the cause and current is the effect. In (b), the other way around.

## Slide 76: Adapter Example Revisited
With our understanding of small-signal analysis, we can revisit our cell phone charger example and easily solve it with just algebra instead of iterations.

## Slide 77: Simple is Beautiful
In this example we study the effect of cell phone pulling some current from the diodes. Using small signal analysis, this is easily done. However, imagine the nightmare, if we were to solve it using non-linear equations.

## Slide 78: Applications of Diode

## Slide 79: Half-Wave Rectifier
A very common application of diodes is half-wave rectification, where either the positive or negative half of the input is blocked.
But, how do we generate a constant output?

## Slide 80: Diode-Capacitor Circuit: Constant Voltage Model
If the resistor in half-wave rectifier is replaced by a capacitor, a fixed voltage output is obtained since the capacitor (assumed ideal) has no path to discharge.

## Slide 81: Diode-Capacitor Circuit: Ideal Model
Note that (b) is just like Vin, only shifted down.

## Slide 82: Diode-Capacitor With Load Resistor
A path is available for capacitor to discharge. Therefore, Vout will not be constant and a ripple exists.

## Slide 83: Behavior for Different Capacitor Values
For large C1, Vout has small ripple.

## Slide 84: Peak to Peak amplitude of Ripple
The ripple amplitude is the decaying part of the exponential.
Ripple voltage becomes a problem if it goes above 5 to 10% of the output voltage.

## Slide 85: Maximum Diode Current
The diode has its maximum current at t1, since that’s when the slope of Vout is the greatest.
This current has to be carefully controlled so it does not damage the device.

## Slide 86: Full-Wave Rectifier
A full-wave rectifier passes both the negative and positive half cycles of the input, while inverting the negative half of the input.
As proved later, a full-wave rectifier reduces the ripple by a factor of two.

## Slide 87: The Evolution of Full-Wave Rectifier
Figures (e) and (f) show the topology that inverts the negative half cycle of the input.

## Slide 88: Full-Wave Rectifier: Bridge Rectifier
The figure above shows a full-wave rectifier, where D1 and D2 pass/invert the negative half cycle of input and D3 and D4 pass the positive half cycle.

## Slide 89: Input/Output Characteristics of a Full-Wave Rectifier (Constant-Voltage Model)
The dead-zone around Vin arises because Vin must exceed 2 VD,ON to turn on the bridge.

## Slide 90: Complete Full-Wave Rectifier
Since C1 only gets ½ of period to discharge, ripple voltage is decreased by a factor of 2. Also (b) shows that each diode is subjected to approximately one Vp reverse bias drop (versus 2Vp in half-wave rectifier).

## Slide 91: Current Carried by Each Diode in the Full-Wave Rectifier

## Slide 92: Summary of Half and Full-Wave Rectifiers
Full-wave rectifier is more suited to adapter and charger applications.

## Slide 93: Voltage Regulator
The ripple created by the rectifier can be unacceptable to sensitive load; therefore, a regulator is required to obtain a very stable output.
Three diodes operate as a primitive regulator.

## Slide 94: Voltage Regulation With Zener Diode
Voltage regulation can be accomplished with Zener diode. Since rd is small, large change in the input will not be reflected at the output.

## Slide 95: Line Regulation VS. Load Regulation
Line regulation is the suppression of change in Vout due to change in Vin (b).
Load regulation is the suppression of change in Vout due to change in load current (c).

## Slide 96: Evolution of AC-DC Converter

## Slide 97: Limiting Circuits
The motivation of having limiting circuits is to keep the signal below a threshold so it will not saturate the entire circuitry.
When a receiver is close to a base station, signals are large and limiting circuits may be required.

## Slide 98: Input/Output Characteristics
Note the clipping of the output voltage.

## Slide 99: Limiting Circuit Using a Diode: Positive Cycle Clipping
As was studied in the past, the combination of resistor-diode creates limiting effect.

## Slide 100: Limiting Circuit Using a Diode: Negative Cycle Clipping

## Slide 101: Limiting Circuit Using a Diode: Positive and Negative Cycle Clipping

## Slide 102: General Voltage Limiting Circuit
Two batteries in series with the antiparalle diodes control the limiting voltages.

## Slide 103: Non-idealities in Limiting Circuits
The clipping region is not exactly flat since as Vin increases, the currents through diodes change, and so does the voltage drop.

## Slide 104: Capacitive Divider

## Slide 105: Waveform Shifter: Peak at -2Vp
As Vin increases, D1 turns on and Vout is zero.
As Vin decreases, D1 turns off, and Vout drops with Vin from zero. The lowest Vout can go is -2Vp, doubling the voltage.

## Slide 106: Waveform Shifter: Peak at 2Vp
Similarly, when the terminals of the diode are switched, a voltage doubler with peak value at 2Vp can be conceived.

## Slide 107: Voltage Doubler
The output increases by Vp, Vp/2, Vp/4, etc in each input cycle, eventually settling to 2 Vp.

## Slide 108: Current thru D1 in Voltage Doubler
Notes: After t1, D1 stops conducting…doesn’t that mean the current running thru it is zero?

## Slide 109: Another Application: Voltage Shifter

## Slide 110: Voltage Shifter (2VD,ON)

## Slide 111: Diode as Electronic Switch
Diode as a switch finds application in logic circuits and data converters.

## Slide 112: Junction Feedthrough
For the circuit shown in part e) of the previous slide, a small feedthrough from input to output via the junction capacitors exists even if the diodes are reverse biased
Therefore, C1 has to be large enough to minimize this feedthrough.

## Slide 113: Chapter 4 Physics of Bipolar Transistors
4.1 General Considerations
4.2 Structure of Bipolar Transistor
4.3 Operation of Bipolar Transistor in Active Mode
4.4 Bipolar Transistor Models
4.5 Operation of Bipolar Transistor in Saturation Mode
4.6 The PNP Transistor

## Slide 114: Bipolar Transistor
In the chapter, we will study the physics of bipolar transistor and derive large and small signal models.

## Slide 115: Voltage-Dependent Current Source
A voltage-dependent current source can act as an amplifier.
If KRL is greater than 1, then the signal is amplified.

## Slide 116: Voltage-Dependent Current Source with Input Resistance
Regardless of the input resistance, the magnitude of amplification remains unchanged.

## Slide 117: Exponential Voltage-Dependent Current Source
A three-terminal exponential voltage-dependent current source is shown above.
Ideally, bipolar transistor can be modeled as such.

## Slide 118: Structure and Symbol of Bipolar Transistor
Bipolar transistor can be thought of as a sandwich of three doped Si regions. The outer two regions are doped with the same polarity, while the middle region is doped with opposite polarity.

## Slide 119: Injection of Carriers
Reverse biased PN junction creates a large electric field that sweeps any injected minority carriers to their majority region.
This ability proves essential in the proper operation of a bipolar transistor.
Notes: The voltage here actually forward bias the PN junction, and there’s no 4.6a), just 4.6.

## Slide 120: Forward Active Region
Forward active region: VBE > 0, VBC < 0.
Figure b) presents a wrong way of modeling figure a).

## Slide 121: Accurate Bipolar Representation
Collector also carries current due to carrier injection from base.

## Slide 122: Carrier Transport in Base

## Slide 123: Collector Current
Applying the law of diffusion, we can determine the charge flow across the base region into the collector.
The equation above shows that the transistor is indeed a voltage-controlled element, thus a good candidate as an amplifier.

## Slide 124: Parallel Combination of Transistors
When two transistors are put in parallel and experience the same potential across all three terminals, they can be thought of as a single transistor with twice the emitter area.

## Slide 125: Simple Transistor Configuration
Although a transistor is a voltage to current converter, output voltage can be obtained by inserting a load resistor at the output and allowing the controlled current to pass thru it.

## Slide 126: Constant Current Source
Ideally, the collector current does not depend on the collector to emitter voltage. This property allows the transistor to behave as a constant current source when its base-emitter voltage is fixed.

## Slide 127: Base Current
Base current consists of two components: 1) Reverse injection of holes into the emitter and 2) recombination of holes with electrons coming from the emitter.

## Slide 128: Emitter Current
Applying Kirchoff’s current law to the transistor, we can easily find the emitter current.

## Slide 129: Summary of Currents

## Slide 130: Bipolar Transistor Large Signal Model
A diode is placed between base and emitter and a voltage controlled current source is placed between the collector and emitter.

## Slide 131: Example: Maximum RL
As RL increases, Vx drops and eventually forward biases the collector-base junction. This will force the transistor out of forward active region.
Therefore, there exists a maximum tolerable collector resistance.

## Slide 132: Characteristics of Bipolar Transistor

## Slide 133: Example: IV Characteristics

## Slide 134: Transconductance
Transconductance, gm shows a measure of how well the transistor converts voltage to current.
It will later be shown that gm is one of the most important parameters in circuit design.

## Slide 135: Visualization of Transconductance
gm can be visualized as the slope of IC versus VBE.
A large IC has a large slope and therefore a large gm.

## Slide 136: Transconductance and Area
When the area of a transistor is increased by n, IS increases by n. For a constant VBE, IC and hence gm increases by a factor of n.

## Slide 137: Transconductance and Ic
The figure above shows that for a given VBE swing, the current excursion around IC2 is larger than it would be around IC1. This is because gm is larger IC2.

## Slide 138: Small-Signal Model: Derivation
Small signal model is derived by perturbing voltage difference every two terminals while fixing the third terminal and analyzing the change in current of all three terminals. We then represent these changes with controlled sources or resistors.

## Slide 139: Small-Signal Model: VBE Change

## Slide 140: Small-Signal Model: VCE Change
Ideally, VCE has no effect on the collector current. Thus, it will not contribute to the small signal model.
It can be shown that VCB has no effect on the small signal model, either.

## Slide 141: Small Signal Example I
Here, small signal parameters are calculated from DC operating point and are used to calculate the change in collector current due to a change in VBE.

## Slide 142: Small Signal Example II
In this example, a resistor is placed between the power supply and collector, therefore, providing an output voltage.

## Slide 143: AC Ground
Since the power supply voltage does not vary with time, it is regarded as a ground in small-signal analysis.

## Slide 144: Early Effect
The claim that collector current does not depend on VCE is not accurate.
As VCE increases, the depletion region between base and collector increases. Therefore, the effective base width decreases, which leads to an increase in the collector current.

## Slide 145: Early Effect Illustration
With Early effect, collector current becomes larger than usual and a function of VCE.

## Slide 146: Early Effect Representation

## Slide 147: Early Effect and Large-Signal Model
Early effect can be accounted for in large-signal model by simply changing the collector current with a correction factor.
In this mode, base current does not change.

## Slide 148: Early Effect and Small-Signal Model

## Slide 149: Summary of Ideas

## Slide 150: Bipolar Transistor in Saturation
When collector voltage drops below base voltage and forward biases the collector-base junction, base current increases and decreases the current gain factor, .

## Slide 151: Large-Signal Model for Saturation Region

## Slide 152: Overall I/V Characteristics
The speed of the BJT also drops in saturation.

## Slide 153: Example: Acceptable VCC Region
In order to keep BJT at least in soft saturation region, the collector voltage must not fall below the base voltage by more than 400mV.
A linear relationship can be derived for VCC and RC and an acceptable region can be chosen.

## Slide 154: Deep Saturation
In deep saturation region, the transistor loses its voltage-controlled current capability and VCE becomes constant.

## Slide 155: PNP Transistor
With the polarities of emitter, collector, and base reversed, a PNP transistor is formed.
All the principles that applied to NPN's also apply to PNP’s, with the exception that emitter is at a higher potential than base and base at a higher potential than collector.

## Slide 156: A Comparison between NPN and PNP Transistors
The figure above summarizes the direction of current flow and operation regions for both the NPN and PNP BJT’s.

## Slide 157: PNP Equations
Early Effect

## Slide 158: Large Signal Model for PNP

## Slide 159: PNP Biasing
Note that the emitter is at a higher potential than both the base and collector.

## Slide 160: Small Signal Analysis

## Slide 161: Small-Signal Model for PNP Transistor
The small signal model for PNP transistor is exactly IDENTICAL to that of NPN. This is not a mistake because the current direction is taken care of by the polarity of VBE.

## Slide 162: Small Signal Model Example I

## Slide 163: Small Signal Model Example II
Small-signal model is identical to the previous ones.

## Slide 164: Small Signal Model Example III
Since during small-signal analysis, a constant voltage supply is considered to be AC ground, the final small-signal model is identical to the previous two.

## Slide 165: Small Signal Model Example IV

## Slide 166: Chapter 5 Bipolar Amplifiers
5.1 General Considerations
5.2 Operating Point Analysis and Design
5.3 Bipolar Amplifier Topologies
5.4 Summary and Additional Examples

## Slide 167: Bipolar Amplifiers

## Slide 168: Voltage Amplifier
In an ideal voltage amplifier, the input impedance is infinite and the output impedance zero.
But in reality, input or output impedances depart from their ideal values.

## Slide 169: Input/Output Impedances
The figure above shows the techniques of measuring input and output impedances.

## Slide 170: Input Impedance Example I
When calculating input/output impedance, small-signal analysis is assumed.

## Slide 171: Impedance at a Node
When calculating I/O impedances at a port, we usually ground one terminal while applying the test source to the other terminal of interest.

## Slide 172: Impedance at Collector
With Early effect, the impedance seen at the collector is equal to the intrinsic output impedance of the transistor (if emitter is grounded).

## Slide 173: Impedance at Emitter
The impedance seen at the emitter of a transistor is approximately equal to one over its transconductance (if the base is grounded).

## Slide 174: Three Master Rules of Transistor Impedances
Rule # 1: looking into the base, the impedance is r if emitter is (ac) grounded.
Rule # 2: looking into the collector, the impedance is ro if emitter is (ac) grounded.
Rule # 3: looking into the emitter, the impedance is 1/gm if base is (ac) grounded and Early effect is neglected.

## Slide 175: Biasing of BJT
Transistors and circuits must be biased because (1) transistors must operate in the active region, (2) their small-signal parameters depend on the bias conditions.

## Slide 176: DC Analysis vs. Small-Signal Analysis
First, DC analysis is performed to determine operating point and obtain small-signal parameters.
Second, sources are set to zero and small-signal model is used.

## Slide 177: Notation Simplification
Hereafter, the battery that supplies power to the circuit is replaced by a horizontal bar labeled Vcc, and input signal is simplified as one node called Vin.

## Slide 178: Example of Bad Biasing
The microphone is connected to the amplifier in an attempt to amplify the small output signal of the microphone.
Unfortunately, there’s no DC bias current running thru the transistor to set the transconductance.

## Slide 179: Another Example of Bad Biasing
The base of the amplifier is connected to Vcc, trying to establish a DC bias.
Unfortunately, the output signal produced by the microphone is shorted to the power supply.

## Slide 180: Biasing with Base Resistor
Assuming a constant value for VBE, one can solve for both IB and IC and determine the terminal voltages of the transistor.
However, bias point is sensitive to  variations.

## Slide 181: Improved Biasing: Resistive Divider
Using resistor divider to set VBE, it is possible to produce an IC that is relatively independent of  if base current is small.

## Slide 182: Accounting for Base Current
With proper ratio of R1 and R2, IC can be insensitive to ; however, its exponential dependence on resistor deviations makes it less useful.

## Slide 183: Emitter Degeneration Biasing
The presence of RE helps to absorb the error in VX so VBE stays relatively constant.
This bias technique is less sensitive to  (I1 >> IB) and VBE variations.

## Slide 184: Design Procedure
Choose an IC to provide the necessary small signal parameters, gm, r, etc.
Considering the variations of R1, R2, and VBE, choose a value for VRE.
With VRE chosen, and VBE calculated, Vx can be determined.
Select R1 and R2 to provide Vx.

## Slide 185: Self-Biasing Technique
This bias technique utilizes the collector voltage to provide the necessary Vx and IB.
One important characteristic of this technique is that collector has a higher potential than the base, thus guaranteeing active operation of the transistor.

## Slide 186: Self-Biasing Design Guidelines
(1) provides insensitivity to  .
(2) provides insensitivity to variation in VBE .

## Slide 187: Summary of Biasing Techniques

## Slide 188: PNP Biasing Techniques
Same principles that apply to NPN biasing also apply to PNP biasing with only polarity modifications.

## Slide 189: Possible Bipolar Amplifier Topologies
Three possible ways to apply an input to an amplifier and three possible ways to sense its output.
However, in reality only three of six input/output combinations are useful.

## Slide 190: Study of Common-Emitter Topology
Analysis of CE Core
Inclusion of Early Effect
Emitter Degeneration
Inclusion of Early Effect
CE Stage with Biasing

## Slide 191: Common-Emitter Topology

## Slide 192: Small Signal of CE Amplifier

## Slide 193: Limitation on CE Voltage Gain
Since gm can be written as IC/VT, the CE voltage gain can be written as the ratio of VRC and VT.
VRC is the potential difference between VCC and VCE, and VCE cannot go below VBE in order for the transistor to be in active region.

## Slide 194: Tradeoff between Voltage Gain and Headroom

## Slide 195: I/O Impedances of CE Stage
When measuring output impedance, the input port has to be grounded so that Vin = 0.

## Slide 196: CE Stage Trade-offs

## Slide 197: Inclusion of Early Effect
Early effect will lower the gain of the CE amplifier, as it appears in parallel with RC.

## Slide 198: Intrinsic Gain
As RC goes to infinity, the voltage gain reaches the product of gm and rO, which represents the maximum voltage gain the amplifier can have.
The intrinsic gain is independent of the bias current.

## Slide 199: Current Gain
Another parameter of the amplifier is the current gain, which is defined as the ratio of current delivered to the load to the current flowing into the input.
For a CE stage, it is equal to .

## Slide 200: Emitter Degeneration
By inserting a resistor in series with the emitter, we “degenerate” the CE stage.
This topology will decrease the gain of the amplifier but improve other aspects, such as linearity, and input impedance.

## Slide 201: Small-Signal Model
Interestingly, this gain is equal to the total load resistance to ground divided by 1/gm plus the total resistance placed in series with the emitter.

## Slide 202: Emitter Degeneration Example I
The input impedance of Q2 can be combined in parallel with RE to yield an equivalent impedance that degenerates Q1.

## Slide 203: Emitter Degeneration Example II
In this example, the input impedance of Q2 can be combined in parallel with RC to yield an equivalent collector impedance to ground.

## Slide 204: Input Impedance of Degenerated CE Stage
With emitter degeneration, the input impedance is increased from r to r + (+1)RE; a desirable effect.

## Slide 205: Output Impedance of Degenerated CE Stage
Emitter degeneration does not alter the output impedance in this case. (More on this later.)

## Slide 206: Capacitor at Emitter
At DC the capacitor is open and the current source biases the amplifier.
For ac signals, the capacitor is short and the amplifier is degenerated by RE.

## Slide 207: Example: Design CE Stage with Degeneration as a Black Box
If gmRE is much greater than unity, Gm is more linear.

## Slide 208: Degenerated CE Stage with Base Resistance

## Slide 209: Input/Output Impedances
Rin1 is more important in practice as RB is often the output impedance of the previous stage.

## Slide 210: Emitter Degeneration Example III

## Slide 211: Output Impedance of Degenerated Stage with VA<
Emitter degeneration boosts the output impedance by a factor of 1+gm(RE||r).
This improves the gain of the amplifier and makes the circuit a better current source.

## Slide 212: Two Special Cases

## Slide 213: Analysis by Inspection
This seemingly complicated circuit can be greatly simplified by first recognizing that the capacitor creates an AC short to ground, and gradually transforming the circuit to a known topology.

## Slide 214: Example: Degeneration by Another Transistor
Called a “cascode”, the circuit offers many advantages that are described later in the book.

## Slide 215: Study of Common-Emitter Topology
Analysis of CE Core
Inclusion of Early Effect
Emitter Degeneration
Inclusion of Early Effect
CE Stage with Biasing

## Slide 216: Bad Input Connection
Since the microphone has a very low resistance that connects from the base of Q1 to ground, it attenuates the base voltage and renders Q1 without a bias current.

## Slide 217: Use of Coupling Capacitor
Capacitor isolates the bias network from the microphone at DC but shorts the microphone to the amplifier at higher frequencies.

## Slide 218: DC and AC Analysis
Coupling capacitor is open for DC calculations and shorted for AC calculations.

## Slide 219: Bad Output Connection
Since the speaker has an inductor, connecting it directly to the amplifier would short the collector at DC and therefore push the transistor into deep saturation.

## Slide 220: Still No Gain!!!
In this example, the AC coupling indeed allows correct biasing. However, due to the speaker’s small input impedance, the overall gain drops considerably.

## Slide 221: CE Stage with Biasing

## Slide 222: CE Stage with Robust Biasing

## Slide 223: Removal of Degeneration for Signals at AC
Capacitor shorts out RE at higher frequencies and removes degeneration.

## Slide 224: Complete CE Stage

## Slide 225: Summary of CE Concepts

## Slide 226: Common Base (CB) Amplifier
In common base topology, where the base terminal is biased with a fixed voltage, emitter is fed with a signal, and collector is the output.

## Slide 227: CB Core
The voltage gain of CB stage is gmRC, which is identical to that of CE stage in magnitude and opposite in phase.

## Slide 228: Tradeoff between Gain and Headroom
To maintain the transistor out of saturation, the maximum voltage drop across RC cannot exceed VCC-VBE.

## Slide 229: Simple CB Example

## Slide 230: Input Impedance of CB
The input impedance of CB stage is much smaller than that of the CE stage.

## Slide 231: Practical Application of CB Stage
To avoid “reflections”, need impedance matching.
CB stage’s low input impedance can be used to create a match with 50 .

## Slide 232: Output Impedance of CB Stage
The output impedance of CB stage is similar to that of CE stage.

## Slide 233: CB Stage with Source Resistance
With an inclusion of a source resistor, the input signal is attenuated before it reaches the emitter of the amplifier; therefore, we see a lower voltage gain.
This is similar to CE stage emitter degeneration; only the phase is reversed.

## Slide 234: Practical Example of CB Stage
An antenna usually has low output impedance; therefore, a correspondingly low input impedance is required for the following stage.

## Slide 235: Realistic Output Impedance of CB Stage
The output impedance of CB stage is equal to RC in parallel with the impedance looking down into the collector.

## Slide 236: Output Impedance of CE and CB Stages
The output impedances of CE, CB stages are the same if both circuits are under the same condition. This is because when calculating output impedance, the input port is grounded, which renders the same circuit for both CE and CB stages.

## Slide 237: Fallacy of the “Old Wisdom”
The statement “CB output impedance is higher than CE output impedance” is flawed.

## Slide 238: CB with Base Resistance
With an addition of base resistance, the voltage gain degrades.

## Slide 239: Comparison of CE and CB Stages with Base Resistance
The voltage gain of CB amplifier with base resistance is exactly the same as that of CE stage with base resistance and emitter degeneration, except for a negative sign.

## Slide 240: Input Impedance of CB Stage with Base Resistance
The input impedance of CB with base resistance is equal to 1/gm plus RB divided by (+1). This is in contrast to degenerated CE stage, in which the resistance in series with the emitter is multiplied by (+1) when seen from the base.

## Slide 241: Input Impedance Seen at Emitter and Base

## Slide 242: Input Impedance Example
To find the RX, we have to first find Req, treat it as the base resistance of Q2 and divide it by (+1).

## Slide 243: Bad Bias Technique for CB Stage
Unfortunately, no emitter current can flow.

## Slide 244: Still No Good
In haste, the student connects the emitter to ground, thinking it will provide a DC current path to bias the amplifier. Little did he/she know that the input signal has been shorted to ground as well. The circuit still does not amplify.

## Slide 245: Proper Biasing for CB Stage

## Slide 246: Reduction of Input Impedance Due to RE
The reduction of input impedance due to RE is bad because it shunts part of the input current to ground instead of to Q1 (and Rc) .

## Slide 247: Creation of Vb
Resistive divider lowers the gain.
To remedy this problem, a capacitor is inserted from base to ground to short out the resistor divider at the frequency of interest.

## Slide 248: Example of CB Stage with Bias
For the circuit shown above, RE >> 1/gm.
R1 and R2 are chosen so that Vb is at the appropriate value and the current that flows thru the divider is much larger than the base current.
Capacitors are chosen to be small compared to 1/gm at the required frequency.

## Slide 249: Emitter Follower (Common Collector Amplifier)

## Slide 250: Emitter Follower Core
When the input is increased by V, output is also increased by an amount that is less than V due to the increase in collector current and hence the increase in potential drop across RE.
However the absolute values of input and output differ by a VBE.

## Slide 251: Small-Signal Model of Emitter Follower
As shown above, the voltage gain is less than unity and positive.

## Slide 252: Unity-Gain Emitter Follower
The voltage gain is unity because a constant collector current (= I1) results in a constant VBE, and hence Vout follows Vin exactly.

## Slide 253: Analysis of Emitter Follower as a Voltage Divider

## Slide 254: Emitter Follower with Source Resistance

## Slide 255: Input Impedance of Emitter Follower
The input impedance of emitter follower is exactly the same as that of CE stage with emitter degeneration. This is not surprising because the input impedance of CE with emitter degeneration does not depend on the collector resistance.

## Slide 256: Emitter Follower as Buffer
Since the emitter follower increases the load resistance to a much higher value, it is suited as a buffer between a CE stage and a heavy load resistance to alleviate the problem of gain degradation.

## Slide 257: Output Impedance of Emitter Follower
Emitter follower lowers the source impedance by a factor of +1 improved driving capability.

## Slide 258: Emitter Follower with Early Effect
Since rO is in parallel with RE, its effect can be easily incorporated into voltage gain and input and output impedance equations.

## Slide 259: Current Gain
There is a current gain of (+1) from base to emitter.
Effectively speaking, the load resistance is multiplied by (+1) as seen from the base.

## Slide 260: Emitter Follower with Biasing
A biasing technique similar to that of CE stage can be used for the emitter follower.
Also, Vb can be close to Vcc because the collector is also at Vcc.

## Slide 261: Supply-Independent Biasing
By putting a constant current source at the emitter, the bias current, VBE, and IBRB are fixed regardless of the supply value.

## Slide 262: Summary of Amplifier Topologies
The three amplifier topologies studied so far have different properties and are used on different occasions.
CE and CB have voltage gain with magnitude greater than one, while follower’s voltage gain is at most one.

## Slide 263: Amplifier Example I
The keys in solving this problem are recognizing the AC ground between R1 and R2, and Thevenin transformation of the input network.

## Slide 264: Amplifier Example II
Again, AC ground/short and Thevenin transformation are needed to transform the complex circuit into a simple stage with emitter degeneration.

## Slide 265: Amplifier Example III
The key for solving this problem is first identifying Req, which is the impedance seen at the emitter of Q2 in parallel with the infinite output impedance of an ideal current source. Second, use the equations for degenerated CE stage with RE replaced by Req.

## Slide 266: Amplifier Example IV
The key for solving this problem is recognizing that CB at frequency of interest shorts out R2 and provide a ground for R1.
R1 appears in parallel with RC and the circuit simplifies to a simple CB stage.

## Slide 267: Amplifier Example V
The key for solving this problem is recognizing the equivalent base resistance of Q1 is the parallel connection of RE and the impedance seen at the emitter of Q2.

## Slide 268: Amplifier Example VI
The key in solving this problem is recognizing a DC supply is actually an AC ground and using Thevenin transformation to simplify the circuit into an emitter follower.

## Slide 269: Amplifier Example VII
Impedances seen at the emitter of Q1 and Q2 can be lumped with RC and RE, respectively, to form the equivalent emitter and collector impedances.

## Slide 270: Chapter 6 Physics of MOS Transistors
6.1 Structure of MOSFET
6.2 Operation of MOSFET
6.3 MOS Device Models
6.4 PMOS Transistor
6.5 CMOS Technology
6.6 Comparison of Bipolar and CMOS Devices

## Slide 271: Chapter Outline

## Slide 272: Metal-Oxide-Semiconductor (MOS) Capacitor
The MOS structure can be thought of as a parallel-plate capacitor, with the top plate being the positive plate, oxide being the dielectric, and Si substrate being the negative plate. (We are assuming P-substrate.)

## Slide 273: Structure and Symbol of MOSFET
This device is symmetric, so either of the n+ regions can be source or drain.

## Slide 274: State of the Art MOSFET Structure
The gate is formed by polysilicon, and the insulator by Silicon dioxide.

## Slide 275: Formation of Channel
First, the holes are repelled by the positive gate voltage, leaving behind negative ions and forming a depletion region. Next, electrons are attracted to the interface, creating a channel (“inversion layer”).

## Slide 276: Voltage-Dependent Resistor
The inversion channel of a MOSFET can be seen as a resistor.
Since the charge density inside the channel depends on the gate voltage, this resistance is also voltage-dependent.

## Slide 277: Voltage-Controlled Attenuator
As the gate voltage decreases, the output drops because the channel resistance increases.
This type of gain control finds application in cell phones to avoid saturation near base stations.

## Slide 278: MOSFET Characteristics
The MOS characteristics are measured by varying VG while keeping VD constant, and varying VD while keeping VG constant.
(d) shows the voltage dependence of channel resistance.

## Slide 279: L and tox Dependence
Small gate length and oxide thickness yield low channel resistance, which will increase the drain current.

## Slide 280: Effect of W
As the gate width increases, the current increases due to a decrease in resistance. However, gate capacitance also increases thus, limiting the speed of the circuit.
An increase in W can be seen as two devices in parallel.

## Slide 281: Channel Potential Variation
Since there’s a channel resistance between drain and source, and if drain is biased higher than the source, channel potential increases from source to drain, and the potential between gate and channel will decrease from source to drain.

## Slide 282: Channel Pinch-Off
As the potential difference between drain and gate becomes more positive, the inversion layer beneath the interface starts to pinch off around drain.
When VD – VG = Vth, the channel at drain totally pinches off, and when VD – VG > Vth, the channel length starts to decrease.

## Slide 283: Channel Charge Density
The channel charge density is equal to the gate capacitance times the gate voltage in excess of the threshold voltage.

## Slide 284: Charge Density at a Point
Let x be a point along the channel from source to drain, and V(x) its potential; the expression above gives the charge density (per unit length).

## Slide 285: Charge Density and Current
The current that flows from source to drain (electrons) is related to the charge density in the channel by the charge velocity.

## Slide 286: Drain Current

## Slide 287: Parabolic ID-VDS Relationship
By keeping VG constant and varying VDS, we obtain a parabolic relationship.
The maximum current occurs when VDS equals to VGS- VTH.

## Slide 288: ID-VDS for Different Values of VGS

## Slide 289: Linear Resistance
At small VDS, the transistor can be viewed as a resistor, with the resistance depending on the gate voltage.
It finds application as an electronic switch.

## Slide 290: Application of Electronic Switches
In a cordless telephone system in which a single antenna is used for both transmission and reception, a switch is used to connect either the receiver or transmitter to the antenna.

## Slide 291: Effects of On-Resistance
To minimize signal attenuation, Ron of the switch has to be as small as possible. This means larger W/L aspect ratio and greater VGS.

## Slide 292: Different Regions of Operation

## Slide 293: How to Determine ‘Region of Operation’
When the potential difference between gate and drain is greater than VTH, the MOSFET is in triode region.
When the potential difference between gate and drain becomes equal to or less than VTH, the MOSFET enters saturation region.

## Slide 294: Triode or Saturation?
When the region of operation is not known, a region is assumed (with an intelligent guess). Then, the final answer is checked against the assumption.

## Slide 295: Channel-Length Modulation
The original observation that the current is constant in the saturation region is not quite correct. The end point of the channel actually moves toward the source as VD increases, increasing ID. Therefore, the current in the saturation region is a weak function of the drain voltage.

## Slide 296:  and L
Unlike the Early voltage in BJT, the channel- length modulation factor can be controlled by the circuit designer.
For long L, the channel-length modulation effect is less than that of short L.

## Slide 297: Transconductance
Transconductance is a measure of how strong the drain current changes when the gate voltage changes.
It has three different expressions.

## Slide 298: Doubling of gm Due to Doubling W/L
If W/L is doubled, effectively two equivalent transistors are added in parallel, thus doubling the current (if VGS-VTH is constant) and hence gm.

## Slide 299: Velocity Saturation
Since the channel is very short, it does not take a very large drain voltage to velocity saturate the charge particles.
In velocity saturation, the drain current becomes a linear function of gate voltage, and gm becomes a function of W.

## Slide 300: Body Effect
As the source potential departs from the bulk potential, the threshold voltage changes.

## Slide 301: Large-Signal Models
Based on the value of VDS, MOSFET can be represented with different large-signal models.

## Slide 302: Example: Behavior of ID with V1 as a Function
Since V1 is connected at the source, as it increases, the current drops.

## Slide 303: Small-Signal Model
When the bias point is not perturbed significantly, small-signal model can be used to facilitate calculations.
To represent channel-length modulation, an output resistance is inserted into the model.

## Slide 304: PMOS Transistor
Just like the PNP transistor in bipolar technology, it is possible to create a MOS device where holes are the dominant carriers. It is called the PMOS transistor.
It behaves like an NMOS device with all the polarities reversed.

## Slide 305: PMOS Equations

## Slide 306: Small-Signal Model of PMOS Device
The small-signal model of PMOS device is identical to that of NMOS transistor; therefore, RX equals RY and hence (1/gm)||ro.

## Slide 307: CMOS Technology
It possible to grow an n-well inside a p-substrate to create a technology where both NMOS and PMOS can coexist.
It is known as CMOS, or “Complementary MOS”.

## Slide 308: Comparison of Bipolar and MOS Transistors
Bipolar devices have a higher gm than MOSFETs for a given bias current due to its exponential IV characteristics.

## Slide 309: Chapter 7 CMOS Amplifiers
7.1 General Considerations
7.2 Common-Source Stage
7.3 Common-Gate Stage
7.4 Source Follower
7.5 Summary and Additional Examples

## Slide 310: Chapter Outline

## Slide 311: MOS Biasing
Voltage at X is determined by VDD, R1, and R2.
VGS can be found using the equation above, and ID can be found by using the NMOS current equation.

## Slide 312: Self-Biased MOS Stage
The circuit above is analyzed by noting M1 is in saturation and no potential drop appears across RG.

## Slide 313: Current Sources
When in saturation region, a MOSFET behaves as a current source.
NMOS draws current from a point to ground (sinks current), whereas PMOS draws current from VDD to a point (sources current).

## Slide 314: Common-Source Stage

## Slide 315: Operation in Saturation
In order to maintain operation in saturation, Vout cannot fall below Vin by more than one threshold voltage.
The condition above ensures operation in saturation.

## Slide 316: CS Stage with =0

## Slide 317: CS Stage with   0
However, Early effect and channel length modulation affect CE and CS stages in a similar manner.

## Slide 318: CS Gain Variation with Channel Length
Since  is inversely proportional to L, the voltage gain actually becomes proportional to the square root of L.

## Slide 319: CS Stage with Current-Source Load
To alleviate the headroom problem, an active current-source load is used.
This is advantageous because a current-source has a high output resistance and can tolerate a small voltage drop across it.

## Slide 320: PMOS CS Stage with NMOS as Load
Similarly, with PMOS as input stage and NMOS as the load, the voltage gain is the same as before.

## Slide 321: CS Stage with Diode-Connected Load
Lower gain, but less dependent on process parameters.

## Slide 322: CS Stage with Diode-Connected PMOS Device
Note that PMOS circuit symbol is usually drawn with the source on top of the drain.

## Slide 323: CS Stage with Degeneration
Similar to bipolar counterpart, when a CS stage is degenerated, its gain, I/O impedances, and linearity change.

## Slide 324: Example of CS Stage with Degeneration
A diode-connected device degenerates a CS stage.

## Slide 325: CS Stage with Gate Resistance
Since at low frequencies, the gate conducts no current, gate resistance does not affect the gain or I/O impedances.

## Slide 326: Output Impedance of CS Stage with Degeneration
Similar to the bipolar counterpart, degeneration boosts output impedance.

## Slide 327: Output Impedance Example (I)
When 1/gm is parallel with rO2, we often just consider 1/gm.

## Slide 328: Output Impedance Example (II)
In this example, the impedance that degenerates the CS stage is rO, instead of 1/gm in the previous example.

## Slide 329: CS Core with Biasing
Degeneration is used to stabilize bias point, and a bypass capacitor can be used to obtain a larger small-signal voltage gain at the frequency of interest.

## Slide 330: Common-Gate Stage
Common-gate stage is similar to common-base stage: a rise in input causes a rise in output. So the gain is positive.

## Slide 331: Signal Levels in CG Stage
In order to maintain M1 in saturation, the signal swing at Vout cannot fall below Vb-VTH.

## Slide 332: I/O Impedances of CG Stage
The input and output impedances of CG stage are similar to those of CB stage.

## Slide 333: CG Stage with Source Resistance
When a source resistance is present, the voltage gain is equal to that of a CS stage with degeneration, only positive.

## Slide 334: Generalized CG Behavior
When a gate resistance is present it does not affect the gain and I/O impedances since there is no potential drop across it ( at low frequencies).
The output impedance of a CG stage with source resistance is identical to that of CS stage with degeneration.

## Slide 335: Example of CG Stage
Diode-connected M2 acts as a resistor to provide the bias current.
Notes: At the gain calculation, the denominator reads Rd in the book instead of Rs

## Slide 336: CG Stage with Biasing
R1 and R2 provide gate bias voltage, and R3 provides a path for DC bias current of M1 to flow to ground.

## Slide 337: Source Follower Stage

## Slide 338: Source Follower Core
Similar to the emitter follower, the source follower can be analyzed as a resistor divider.

## Slide 339: Source Follower Example
In this example, M2 acts as a current source.

## Slide 340: Output Resistance of Source Follower
The output impedance of a source follower is relatively low, whereas the input impedance is infinite ( at low frequencies); thus, a good candidate as a buffer.

## Slide 341: Source Follower with Biasing
RG sets the gate voltage to VDD, whereas RS sets the drain current.
The quadratic equation above can be solved for ID.

## Slide 342: Supply-Independent Biasing
If Rs is replaced by a current source, drain current ID becomes independent of supply voltage.

## Slide 343: Example of a CS Stage (I)
M1 acts as the input device and M2, M3 as the load.

## Slide 344: Example of a CS Stage (II)
M1 acts as the input device, M3 as the source resistance, and M2 as the load.

## Slide 345: Examples of CS and CG Stages
With the input connected to different locations, the two circuits, although identical in other aspects, behave differently.

## Slide 346: Example of a Composite Stage (I)
By replacing the left side with a Thevenin equivalent, and recognizing the right side is actually a CG stage, the voltage gain can be easily obtained.

## Slide 347: Example of a Composite Stage (II)
This example shows that by probing different places in a circuit, different types of output can be obtained.
Vout1 is a result of M1 acting as a source follower whereas Vout2 is a result of M1 acting as a CS stage with degeneration.
Notes: For vout2, the denominator has an extra 1/gm1

## Slide 348: Chapter 8 Operational Amplifier as A Black Box
8.1 General Considerations
8.2 Op-Amp-Based Circuits
8.3 Nonlinear Functions
8.4 Op-Amp Nonidealities
8.5 Design Examples

## Slide 349: Chapter Outline

## Slide 350: Basic Op Amp
Op amp is a circuit that has two inputs and one output.
It amplifies the difference between the two inputs.

## Slide 351: Inverting and Non-inverting Op Amp
If the negative input is grounded, the gain is positive.
If the positive input is grounded, the gain is negative.

## Slide 352: Ideal Op Amp
Infinite gain
Infinite input impedance
Zero output impedance
Infinite speed

## Slide 353: Virtual Short
Due to infinite gain of op amp, the circuit forces Vin2 to be close to Vin1, thus creating a virtual short.

## Slide 354: Unity Gain Amplifier

## Slide 355: Op Amp with Supply Rails
To explicitly show the supply voltages, VCC and VEE are shown.
In some cases, VEE is zero.

## Slide 356: Noninverting Amplifier (Infinite A0)
A noninverting amplifier returns a fraction of output signal thru a resistor divider to the negative input.
With a high Ao, Vout/Vin depends only on ratio of resistors, which is very precise.

## Slide 357: Noninverting Amplifier (Finite A0)
The error term indicates the larger the closed-loop gain, the less accurate the circuit becomes.

## Slide 358: Extreme Cases of R2 (Infinite A0)
If R2 is zero, the loop is open and Vout /Vin is equal to the intrinsic gain of the op amp.
If R2 is infinite, the circuit becomes a unity-gain amplifier and Vout /Vin becomes equal to one.

## Slide 359: Inverting Amplifier
Infinite A0 forces the negative input to be a virtual ground.
Notes: I think the resistors positions in the equations should be reversed.

## Slide 360: Another View of Inverting Amplifier
Inverting
Noninverting

## Slide 361: Gain Error Due to Finite A0
The larger the closed loop gain, the more inaccurate the circuit is.

## Slide 362: Complex Impedances Around the Op Amp
The closed-loop gain is still equal to the ratio of two impedances.

## Slide 363: Integrator
Notes: The equation that defines the time domain behavior of the integrator is not correct..since Vin over R1, not Vout

## Slide 364: Integrator with Pulse Input

## Slide 365: Comparison of Integrator and RC Lowpass Filter
The RC low-pass filter is actually a “passive” approximation to an integrator.
With the RC time constant large enough, the RC filter output approaches a ramp.
Notes: The filter’s output looks like a ln() response, rather than an exponential response.

## Slide 366: Lossy Integrator
When finite op amp gain is considered, the integrator becomes lossy as the pole moves from the origin to -1/[(1+A0)R1C1].
It can be approximated as an RC circuit with C boosted by a factor of A0+1.

## Slide 367: Differentiator

## Slide 368: Differentiator with Pulse Input

## Slide 369: Comparison of Differentiator and High-Pass Filter
The RC high-pass filter is actually a passive approximation to the differentiator.
When the RC time constant is small enough, the RC filter approximates a differentiator.

## Slide 370: Lossy Differentiator
When finite op amp gain is considered, the differentiator becomes lossy as the zero moves from the origin to –(A0+1)/R1C1.
It can be approximated as an RC circuit with R reduced by a factor of (A0+1).

## Slide 371: Op Amp with General Impedances
This circuit cannot operate as ideal integrator or differentiator.

## Slide 372: Voltage Adder
If Ao is infinite, X is pinned at ground, currents proportional to V1 and V2 will flow to X and then across RF to produce an output proportional to the sum of two voltages.
If R1 = R2=R
Ao

## Slide 373: Precision Rectifier
When Vin is positive, the circuit in b) behaves like that in a), so the output follows input.
When Vin is negative, the diode opens, and the output drops to zero. Thus performing rectification.

## Slide 374: Inverting Precision Rectifier
When Vin is positive, the diode is on, Vy is pinned around VD,on, and Vx at virtual ground.
When Vin is negative, the diode is off, Vy goes extremely negative, and Vx becomes equal to Vin.

## Slide 375: Logarithmic Amplifier
By inserting a bipolar transistor in the loop, an amplifier with logarithmic characteristic can be constructed.
This is because the current to voltage conversion of a bipolar transistor is a natural logarithm.

## Slide 376: Square-Root Amplifier
By replacing the bipolar transistor with a MOSFET, an amplifier with a square-root characteristic can be built.
This is because the current to voltage conversion of a MOSFET is square-root.

## Slide 377: Op Amp Nonidealities: DC Offsets
Offsets in an op amp that arise from input stage mismatch cause the input-output characteristic to shift in either the positive or negative direction (the plot displays positive direction).

## Slide 378: Effects of DC Offsets
As it can be seen, the op amp amplifies the input as well as the offset, thus creating errors.

## Slide 379: Saturation Due to DC Offsets
Since the offset will be amplified just like the input signal, output of the first stage may drive the second stage into saturation.

## Slide 380: Offset in Integrator
A resistor can be placed in parallel with the capacitor to “absorb” the offset. However, this means the closed-loop transfer function no longer has a pole at origin.

## Slide 381: Input Bias Current
The effect of bipolar base currents can be modeled as current sources tied from the input to ground.

## Slide 382: Effects of Input Bias Current on Noninverting Amplifier
It turns out that IB1 has no effect on the output and IB2 affects the output by producing a voltage drop across R1.

## Slide 383: Input Bias Current Cancellation
We can cancel the effect of input bias current by inserting a correction voltage in series with the positive terminal.
In order to produce a zero output, Vcorr=-IB2(R1||R2).

## Slide 384: Correction for  Variation
Since the correction voltage is dependent upon , and  varies with process, we insert a parallel resistor combination in series with the positive input. As long as IB1= IB2, the correction voltage can track the  variation.

## Slide 385: Effects of Input Bias Currents on Integrator
Input bias current will be integrated by the integrator and eventually saturate the amplifier.

## Slide 386: Integrator’s Input Bias Current Cancellation
By placing a resistor in series with the positive input, integrator input bias current can be cancelled.
However, the output still saturates due to other effects such as input mismatch, etc.

## Slide 387: Speed Limitation
Due to internal capacitances, the gain of op amps begins to roll off.

## Slide 388: Bandwidth and Gain Tradeoff
Having a loop around the op amp (inverting, noninverting, etc) helps to increase its bandwidth. However, it also decreases the low frequency gain.

## Slide 389: Slew Rate of Op Amp
In the linear region, when the input doubles, the output and the output slope also double. However, when the input is large, the op amp slews so the output slope is fixed by a constant current source charging a capacitor.
This further limits the speed of the op amp.

## Slide 390: Comparison of Settling with and without Slew Rate
As it can be seen, the settling speed is faster without slew rate (as determined by the closed-loop time constant).

## Slide 391: Slew Rate Limit on Sinusoidal Signals
As long as the output slope is less than the slew rate, the op amp can avoid slewing.
However, as operating frequency and/or amplitude is increased, the slew rate becomes insufficient and the output becomes distorted.

## Slide 392: Maximum Op Amp Swing
To determine the maximum frequency before op amp slews, first determine the maximum swing the op amp can have and divide the slew rate by it.

## Slide 393: Nonzero Output Resistance
In practical op amps, the output resistance is not zero.
It can be seen from the closed loop gain that the nonzero output resistance increases the gain error.

## Slide 394: Design Examples
Many design problems are presented at the end of the chapter to study the effects of finite loop gain, restrictions on peak to peak swing to avoid slewing, and how to design for a certain gain error.